ECEn 631 Camera Calibration & Distortion Correction – HW 2
Seth Nielsen

Task 1

Corner detection image:

This is an image where OpenCV’s findChessboardCorners() and drawChessboardCorners() functions were used to detect and circle the inner corners of a chessboard.
Task 2

Intrinsic parameters:
[[1145.8, 0, 328.5],
 [0, 1144.2, 222.3],
 [0, 0, 1]]

Distortion parameters:
[ -0.256, -0.0235, -0.00139, -0.00140, 2.14]

Focal length:
Assuming an 8.5 mm lens, a 7.4 μm x 7.4 μm pixel size, and a 648x488 pixel CMOS sensor, the focal length will be:

648 pix/4.8 mm = 135 pixels/mm
fx = fy = 8.5 mm x 135 pixels/mm = 1147.5 pixels

This matches well with the fsx and fsy values found in the intrinsic parameters matrix.
Task 3

Absolute difference images:

Far

Turned

Close

These images show the difference between the original (distorted) image and the undistorted image, which is corrected for lens distortion.
Task 4

Rotation matrix (R):

[[ 0.73571429, -0.6771657, 0.01308065]
 [-0.00334617, -0.02294706, -0.99973108]
 [ 0.67728376, 0.73547267, -0.01914839]]

Translation matrix (T):

[[-0.0048875 ]
 [10.48000795]
 [46.70723134]]

These are the rotation and translation matrices for estimating the pose of a chessboard.
Task 5

Intrinsic parameters of my laptop’s webcam:

[[ 729.5, 0., 356.1],
 [0., 698.0, 279.0],
 [0., 0., 1. ]]

Distortion parameters:

[ -0.104, 1.01, -0.00114, 0.00570, -2.16]

Task 6

Absolute difference image:

This is the absolute difference image between a raw frame taken from my laptop’s webcam and the same frame corrected for lens distortion.